Inputs for IIA Newsletter (Mar-10)

In the last few months there has been very significant progress on the development of the detector system for UVIT. Some of the highlights are briefly presented here.

EMI/EMC test on Engineering Model UVIT Detector System

Engineering Model of UVIT detector System had gone under EMI/EMC test at ISRO Satellite Centre (ISAC) in the first week of Feb 2010. The EM detector system has already qualified the EMI/EMC test at Canadian Space Agency (CSA), Canada. At ISAC, ISRO we had to repeat this test while simulating a more true to ASTROSAT grounding scheme. Results of EMI-EMC test appear satisfactory, but a full analysis of the test results is yet to be completed.

Arrival of Flight Model Detector System:

Flight Model detector system arrived at IIA, CREST in the last week of February, from CSA. During the first two weeks of March, electrical functional/performance tests have been successfully completed on all the three (Visible, Near UV, and Far UV) detectors.

Figure 1: All the 3 detector systems (FUV, NUV and VIS) are placed in Class 10,000 at CREST, for electrical functional/performance tests.

After the functional and performance tests, Quantum Efficiency tests have been done on Far UV and Near UV detectors. The results are shown in Figure 3 and 4.

Figure 2: QE (%) test setup of FM detector in class 10,000 area at CREST; in order to minimize any contamination of the detector-window a Class 100 air-blower is used on the Camera Proximity Unit ( front end of the detector system).

Figure 3: QE (%) test result of FM detector (NUV Channel)

Figure 4: QE (%) test result of FM detector (FUV Channel)

# Text boxes

CPU (Camera Proximity Unit)

HVU (High Voltage Unit)

Vacuum Tank

with the UV source and beam-optics

EU (Electronics Unit)